for="project in objects"

Projet.Client.NomAffiche
Project.Client.Adresse
Project.Client.NPA Project.Client.Ville

REPORT no	Project.Nom	La Chaux-de-Fonds, le function="format_py3o_datetime_to_date(project.write_date)"
Your / Ref.	Project.RéférenceClient
Reception	function="format_py3o_date(project.reception_date)"
Return samples	if="project.send_sample_back==True" / Yes / /if / if="project.send_sample_back==False" / No / /if

- NICKEL RELEASE ACCORDING TO EN ISO 1811: 2011 WITH A1: 2015 ACCREDITED METHOD ACCORDING TO STANDARD ISO 17025
  function="format_py3o_html(project.analyze_sample)"
- TEST
for="task in project.task_ids"
  - Test Nr Projet.Tâche.Nom
/for
- RESULTS: NICKEL RELEASE
if="project.conformity == 'conform'" / X / /if	COMPLIANT	if="project.conformity == 'not_conform'" / X / /if	NON COMPLIANT

Interpretation of the result according to EN ISO 1811 with A1: 2015 :

- The result is less to 0.88 μg/cm2/week: COMPLIANT
- The result is equal or superior to 0.88 μg/cm2/week: NON COMPLIANT
- OBSERVATIONS
- REMARKS
  REACH Annex XVII, (Entrance N°27 Nickel and its compounds) specifies that the nickel release should not exceed 0.5 [μg/cm2/week] in articles intended to come into direct and prolonged contact with the skin.
  Amendment A1 takes into account the measurement uncertainty of the method of 46% making an article non compliant when it releases 0.88 μg/cm2/week. To be placed on the market, an article in must release a nickel concentration below 0.88 μg/cm2/week.
  There is a potential risk of allergy from 0.3 μg/cm2/week.
  The calculation of the surface is projected surface of tested part, increasing the value of nickel release.
  The result contained in this report relates only the parts under review.

function="format_py3o_html(project.conclusion)"

METALLO-TESTS SA

Project.Responsable1	Project.Responsable2

/for