for="project in objects"
Projet.Client.NomAffiche
Project.Client.Adresse
Project.Client.NPA Project.Client.Ville

REPORT no	Project.Nom	La Chaux-de-Fonds, function="format_py3o_datetime(project.write_date)"
V / Réf.	Project.RéférenceClient
Reception	function="format_py3o_date(project.reception_date)"
Return samples	if="project.send_sample_back==True" / Yes / /if / if="project.send_sample_back==False" / No / /if

- NICKEL RELEASE ACCORDING TO EN ISO 1811 :2011 WITH A1 :2015 ACCREDITED METHOD ACCORDING TO STANDARD ISO 17025
  function="format_py3o_html(project.analyze_sample)"
- TESTS
for="task in project.task_ids"
  - Essai nº Projet.Tâche.Nom
/for
RESULTS: NICKEL RELEASE
if="project.conformity == 'conform'" / X / /if	COMPLIANT	if="project.conformity == 'not_conform'" / X / /if	NON COMPLIANT

OBSERVATIONS
REMARKS
Interpretation of the result according to EN ISO 1811 with A1 :2015 :
- The result is less to 0.88 μg/cm2/week: COMPLIANT
- The result is equal or superior to 0.88 μg/cm2/week: NON COMPLIANT

REACH Annex XVII, (Entrance N°27 Nickel and its compounds) specifies that the nickel release should not exceed 0.5 [μg/cm2/week] in articles intended to come into direct and prolonged contact with the skin.

Amendment A1 takes into account the measurement uncertainty of the method of 46% making an article non compliant when it releases 0.88 μg/cm2/week. To be placed on the market, an article in must release a nickel concentration below 0.88 μg/cm2/week.

There is a potential risk of allergy from 0.3 μg/cm2/week.
The calculation of the surface is always an estimate below the real area, increasing the value of nickel release.
The result contained in this report relates only the parts under review.

function="format_py3o_html(project.conclusion)"

METALLO-TESTS SA	METALLO-TESTS SA

Project.Responsable1	Project.Responsable2

/for